## Slide 1
Cadence genus

## Slide 2: AGENDA
PRACTICE WITH LAB 1
PRACTICE WITH LAB 3
SEARCH FOR MAXIMUM OPERATING FREQUENCY OF DESIGN & SUBMISSION DATA

## Slide 3
LAB structure

## Slide 4: LAB DIRECTORY STRUCTURE (1/2)
To run the lab, it requires 4 below data
    RTL DESIGN (*.v)
    SYNTHESIS LIBRARY (*.lib)
    SYNTHESIS CONSTRAINT
    SAMPLE ENVIRONMENT
Please copy Sample Environment Kit from Cadence to your each synthesis working folder
      [rvc@localhost ~]$
      cd /home/{group}??/vlsi/${Student_ID}/work/synthesis_env
      [rvc@localhost synthesis_env]$
      cp -rf /home/share_file/cadence/installs/Genus_CUI_RAK/ ./Genus_BoundFlasher

## Slide 5: LAB DIRECTORY STRUCTURE (2/2)
      [rvc@localhost synthesis_env]$
      ls Genus_BoundFlasher
①
②
③
④
①
②
③
④

## Slide 6
LAB 1: BASIC GENUS FLOW

## Slide 7: LAB1: BASIC GENUS FLOW
Step 1: Prepare your RTL and put to below path ./Genus_BoundFlasher/RTL/
Step 2: Prepare constraints as below at
      # Set the current design
      current_design bound_flasher
      create_clock -name "clk" -add -period 5.0 -waveform {0.0 2.5} [get_ports clk]
      set_input_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports flick]
      set_input_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports rst_n]
      set_output_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports lamp ]
      set_max_fanout 15.000 [current_design]
      set_max_transition 1.2 [current_design]
      [rvc@localhost synthesis_env]$
      vi ./Genus_BoundFlasher/constraints/bound_flasher_gate.sdc
      bound_flasher_gate.sdc
Design Module Name
Clock Port Name
Inputs / Outputs

## Slide 8: LAB1: BASIC GENUS FLOW
Step 3: Modify environment a bit to map current design
      ##############################################################################
      ## Preset global variables and attributes
      ##############################################################################
      . . .
      set DESIGN bound_flasher
      ####################################################################
      ## Load Design
      ####################################################################
      read_hdl "bound_flasher.v"
      elaborate $DESIGN
      . . .
      ####################################################################
      ## Constraints Setup
      ####################################################################
      read_sdc ../constraints/bound_flasher_gate.sdc
      . . .
      #######################################################################################################
      ## Optimize Netlist
      #######################################################################################################
      . . .
      write_hdl > ${_OUTPUTS_PATH}/${DESIGN}_m.v
      #################################
      ### write_do_lec
      #################################
      quit
      [rvc@localhost synthesis_env]$
      vi ./Genus_BoundFlasher/LAB1/run.tcl
Design Module Name
RTL File Name
Constraint File Name
NETLIST File (Important)
Quit at end

## Slide 9: LAB1: BASIC GENUS FLOW
Step 4: Source Genus & license files. Then, execute Synthesis
The following message will show in the Genus session when synthesis is done:
      [rvc@localhost synthesis_env]$ cd /home/share_file/cadence [rvc@localhost cadence]$ source add_path [rvc@localhost cadence]$ source add_license
      [rvc@localhost cadence]$ cd -
      [rvc@localhost synthesis_env]$ cd ./LAB1/
      [rvc@localhost LAB1]$ genus -f run.tcl | tee -i sync.log

## Slide 10: LAB1: BASIC GENUS FLOW
Step 5: Check synthesis Log file to confirm no “Error” occur
If it occurs “Error”, you need to resolved all Error before go to next step.
      [rvc@localhost LAB1]$ vi sync.log
NG
OK

## Slide 11: LAB1: BASIC GENUS FLOW
Step 6: Check Synthesis Report
      [rvc@localhost synthesis_env]$ cd ./LAB1/
      [rvc@localhost LAB1]$ vi reports??/final_area.rpt //Check Design Area
      [rvc@localhost LAB1]$ vi reports??/final_qor.rpt //Check QoR Information
      [rvc@localhost LAB1]$ vi reports??/final_time.rpt //Check Detail Timing Path
Critical Path Slack (CPS)(unit:ps) >= 0 proves QUALIFIED NETLIST
NG
OK

## Slide 12: LAB1: BASIC GENUS FLOW
Step 7: Prepare script to load NETLIST
      [rvc@localhost LAB1]$ vi gui.tcl //Create new file
      set DESIGN bound_flasher
      ###############################################################
      ## Library setup
      ###############################################################
      read_libs "../LIB/slow.lib ../LIB/pll.lib ../LIB/CDK_S128x16.lib ../LIB/CDK_S256x16.lib ../LIB/CDK_R512x16.lib "
      read_physical -lef " ../LEF/gsclib045_tech.lef ../LEF/gsclib045_macro.lef ../LEF/pll.lef ../LEF/CDK_S128x16.lef ../LEF/CDK_S256x16.lef ../LEF/CDK_R512x16.lef "
      ####################################################################
      ## Load Design
      ####################################################################
      read_hdl "./outputs/bound_flasher_m.v"
      elaborate $DESIGN
      gui.tcl
Suppose that NETLIST is stored at LAB1/outputs/bound_flasher_m.v
Design Module Name

## Slide 13: LAB1: BASIC GENUS FLOW
Step 8: Invoke NETLIST Schematic Window
      [rvc@localhost LAB1]$ genus -f gui.tcl -gui //Open Genus GUI and load NETLIST
Righ Click

## Slide 14
LAB 3: LOW-POWER SYNTHESIS

## Slide 15: LAB3: running low-power synthesis
Step 1: Prepare your RTL and put to below path ./Genus_BoundFlasher/RTL/
Step 2: Prepare constraints as below at
      # Set the current design
      current_design bound_flasher
      create_clock -name "clk" -add -period 5.0 -waveform {0.0 2.5} [get_ports clk]
      set_input_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports flick]
      set_input_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports rst_n]
      set_output_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports lamp ]
      set_max_fanout 15.000 [current_design]
      set_max_transition 1.2 [current_design]
      [rvc@localhost synthesis_env]$
      vi ./Genus_BoundFlasher/constraints/bound_flasher_gate.sdc
      bound_flasher_gate.sdc
Design Module Name
Clock Port Name
Inputs / Outputs

## Slide 16: LAB3: running low-power synthesis
Step 3: Modify environment a bit to map current design
      ##############################################################################
      ## Preset global variables and attributes
      ##############################################################################
      . . .
      set DESIGN bound_flasher
      ####################################################################
      ## Load Design
      ####################################################################
      read_hdl "bound_flasher.v"
      elaborate $DESIGN
      . . .
      ####################################################################
      ## Constraints Setup
      ####################################################################
      read_sdc ../constraints/bound_flasher_gate.sdc
      . . .
      #######################################################################################################
      ## Optimize Netlist
      #######################################################################################################
      . . .
      write_hdl > ${_OUTPUTS_PATH}/${DESIGN}_m.v
      #################################
      ### write_do_lec
      #################################
      quit
      [rvc@localhost synthesis_env]$
      vi ./Genus_BoundFlasher/LAB3/run.tcl
Design Module Name
RTL File Name
Constraint File Name
NETLIST File (Important)
Quit at end

## Slide 17: LAB3: running low-power synthesis
Step 4: Setting Power Optimization Attributes
Low-power synthesis is included as part of the synthesis process.
      ###############################################################
      ## Library setup
      ###############################################################
      set_db / .lp_insert_clock_gating true
      set_db / .leakage_power_effort medium
      #######################################################################################
      ## Leakage/Dynamic power/Clock Gating setup.
      #######################################################################################
      #set_db "design:$DESIGN" .lp_clock_gating_cell [vfind /lib* -lib_cell <cg_libcell_name>]
      set_db "design:$DESIGN" .max_leakage_power 0.0
      set_db "design:$DESIGN" .lp_power_optimization_weight 0.5 ;#<value from 0 to 1>
      set_db "design:$DESIGN" .max_dynamic_power 100
Enable Clock-Gating features. It must be enable before ELABORATE command
Set the leakage power optimization effort
Specify the optimization weight for dynamic power versus leakage power.
Set the maximum dynamic power attribute

## Slide 18: LAB3: running low-power synthesis
Step 5: Source Genus & license files. Then, execute Synthesis
The following message will show in the Genus session when synthesis is done:
      [rvc@localhost synthesis_env]$ cd /home/share_file/cadence [rvc@localhost cadence]$ source add_path [rvc@localhost cadence]$ source add_license
      [rvc@localhost cadence]$ cd -
      [rvc@localhost synthesis_env]$ cd ./LAB3/
      [rvc@localhost LAB3]$ genus -f run.tcl | tee -i sync.log

## Slide 19: LAB3: running low-power synthesis
Step 6: Check synthesis Log file to confirm no “Error” occur
If it occurs “Error”, you need to resolved all Error before go to next step.
      [rvc@localhost LAB3]$ vi sync.log
NG
OK

## Slide 20: LAB3: running low-power synthesis
Step 7: Check Synthesis Report (AS LAB 1)
      [rvc@localhost synthesis_env]$ cd ./LAB3/
      [rvc@localhost LAB3]$ vi reports??/final_area.rpt //Check Design Area
      [rvc@localhost LAB3]$ vi reports??/final_qor.rpt //Check QoR Information
      [rvc@localhost LAB3]$ vi reports??/final_time.rpt //Check Detail Timing Path
Critical Path Slack (CPS)(unit:ps) >= 0 proves QUALIFIED NETLIST
NG
OK

## Slide 21: LAB3: running low-power synthesis
Step 8: Prepare script to load NETLIST
      [rvc@localhost LAB3]$ vi gui.tcl //Create new file
      set DESIGN bound_flasher
      ###############################################################
      ## Library setup
      ###############################################################
      read_libs "../LIB/slow.lib ../LIB/pll.lib ../LIB/CDK_S128x16.lib ../LIB/CDK_S256x16.lib ../LIB/CDK_R512x16.lib "
      read_physical -lef " ../LEF/gsclib045_tech.lef ../LEF/gsclib045_macro.lef ../LEF/pll.lef ../LEF/CDK_S128x16.lef ../LEF/CDK_S256x16.lef ../LEF/CDK_R512x16.lef "
      ####################################################################
      ## Load Design
      ####################################################################
      read_hdl "./outputs/bound_flasher_m.v"
      elaborate $DESIGN
      gui.tcl
Suppose that NETLIST is stored at LAB3/outputs/bound_flasher_m.v
Design Module Name

## Slide 22: LAB3: running low-power synthesis
Step 9: Invoke NETLIST Schematic Window
      [rvc@localhost LAB3]$ genus -f gui.tcl -gui //Open Genus GUI and load NETLIST
Righ Click

## Slide 23
Search maximum design frequency &
SUBMISSION DATA

## Slide 24: Search maximum design frequency
Please re-use LAB1 and change Design Frequency until MAX while Critical Path Slave >= 0
Change Design Constraints and re-run Synthesis as LAB1
      # Set the current design
      current_design bound_flasher
      create_clock -name "clk" -add -period 5.0 -waveform {0.0 2.5} [get_ports clk]
      set_input_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports flick]
      set_input_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports rst_n]
      set_output_delay -clock [get_clocks clk] -add_delay 2.5 [get_ports lamp ]
      set_max_fanout 15.000 [current_design]
      set_max_transition 1.2 [current_design]
      [rvc@localhost synthesis_env]$
      vi ./Genus_BoundFlasher/constraints/bound_flasher_gate.sdc
      bound_flasher_gate.sdc
Change Design Clock Period (ns)
Inputs / Outputs
Change so that Duty Cycle = 50%
Change so that it is 50% of Design Clock Period (ns)

## Slide 25: Submission data
After re-synthesize with Maximum frequency, please submit below data: (Note that LAB1 & LAB3 just for practice, no need to submit any data related to them)
  Netlist: outputs??/${DESIGN}_m.v (Ex: bound_flasher_m.v)
  Area report: reports??/final_area.rpt
  QoR report: reports??/final_qor.rpt
  Timing report: reports??/final_time.rpt

## Slide 26
Renesas.com